## Slide 1: Education evenings 2016
Practical introduction to groundwater modelling
Computer exercises
03 04 What else?

## Slide 2: ModelMuse
Much more functionality to be discovered!
Refer to:
the ModelMuse manual
the ModelMuse videos
the ModelMuse help

## Slide 3: ModelMuse and MODFLOW
Many more packages available to use
Compatibility with MODFLOW versions other than the core MODFLOW-2005
  MODFLOW-LGR
  MODFLOW-NWT
  MODFLOW-OWHM
  MODFLOW-CFP

## Slide 4: MODFLOW packages
We only used a few…

## Slide 5: MODFLOW-LGR
MODFLOW-LGR allows smaller parts of a larger model domain to be refined without refining the entire model.

## Slide 6: MODFLOW-NWT
MODFLOW-NWT is a Newton-Raphson formulation for MODFLOW-2005 to improve solution of unconfined groundwater-flow problems.
It is intended for solving problems involving drying and rewetting nonlinearities of the unconfined groundwater-flow equation.

## Slide 7: MODFLOW-OWHM
MODFLOW-OWHM, or the One-Water Hydrologic Flow Model, is an integrated hydrologic flow model (IHM).
It is designed for the analysis of a broad range of issues related to the combined use of groundwater and surface water.
It allows the simulation, analysis, and management of human and natural water movement within a physically-based supply-and-demand framework.

## Slide 8: MODFLOW-CFP
MODFLOW-CFP has the ability to simulate turbulent or laminar groundwater flow conditions by:
coupling the traditional groundwater flow equation with formulations for a 1-dimensional discrete network of cylindrical pipes (Mode 1, CFPM1),
inserting a high-conductivity flow layer that can switch between laminar and turbulent flow (Mode 2, CFPM2), or
simultaneously coupling a discrete pipe network while inserting a high-conductivity flow layer that can switch between laminar and turbulent flow (Mode 3, CFPM3).

## Slide 9: Beyond the GUI
Several scripting language interfaces to MODFLOW exist, or are in development:
Flopy (python)
Mflab (matlab)
RMODFLOW (R)
These are useful for:
Parameter estimation or uncertainty quantification that goes beyond MODFLOW parameters and/or UCODE algorithms
Geostatistical simulation for e.g. material properties
Quickly converting database information to input files
Reproducible reporting
…

## Slide 10: ModelMuse and PHAST
PHAST is a Computer Program for Simulating
Groundwater Flow,
Solute Transport, and
Multicomponent Geochemical Reactions,
for which it uses PHREEQC.

## Slide 11: ModelMuse and SUTRA
SUTRA is a model for
saturated-unsaturated,
variable-density ground-water flow,
with solute
or energy transport.

## Slide 12: Education evenings 2016
Practical introduction to groundwater modelling
Computer exercises
03 04 What else?
Questions? Found an error? Please contact B. Rogiers at brogiers@sckcen.be.