## Slide 1: Education evenings 2018
Practical introduction to groundwater modelling
Computer exercises
04 01 Grid design

## Slide 2: Purpose
In this exercise, we will
modify the default grid manually,
specify the grid design using objects,
change the active part of the grid,
and increase vertical discretization of the default Layer Groups,
in order to get acquainted with some of the ModelMuse grid design possibilities.

## Slide 3: Set initial grid
2. We are now at the initial grid window
1. Start ModelMuse, create a new MODFLOW model and set the projection to "NA".
3. where we can specify the number of cells in each direction
4. the grid origin, angle and vertical exaggeration
5. the horizontal cell dimensions
6. and the layer group names and bottom elevations.
7. Accept the defaults and click Finish.

## Slide 4: Modify the grid manually
2. Delete grid lines
3. Drag grid lines
5. Add horizontal grid line
6. Subdivide grid cells
7. Set spacing of selected elements
8. Drag to rotate grid
4. Add vertical grid line
1. The grid toolbar provides different tools to do so.
9. Take a moment to familiarize yourself with the different tools.
10. Note you can also use some of the tools in the Top and Side views.

## Slide 5: Skip creating a grid
2. We have used the initial grid window before
3. Therefore skip creating a grid at this point by clicking the No grid button
1. Start ModelMuse again, create a new MODFLOW model and set the projection to "NA".

## Slide 6: Use object to set grid cell size
1. Select Create polygon object, and
3. Therefore skip creating a grid at this point by clicking the No grid button
2. Draw a polygon like this.
3. In the Object Properties dialog box, check Use to set grid cell size
4. And set it to 10 (or another reasonable number if your polygon size is not really compatible with it).
5. Click OK.

## Slide 7: Generate grid
1. Click the Generate grid button
2. Leave the default options, and press OK.
3. This is what you should get.

## Slide 8: Refine grid with object
2. Generate the grid again without the Smooth grid option.
3. Then press undo and generate the grid with the Smooth grid option to see the difference.
1. Add a polygon, and use it to set grid cell size to 2.

## Slide 9: Set active part of grid with object
1. Set the Active data set default formula to False
2. Then modify the data set with the largest polygon. Make sure it has the correct Z coordinates!

## Slide 10: Visualize active part of grid
1. Colour the grid with the active data set, or
2. Select Show or hide 2D gridlines|Show Active

## Slide 11: Activate Middle and Lower Aquifers again
1. Check if the second and third layer are active.
2. If not, set the Lower Z-coordinate of the largest polygon to Lower_Aquifer_Bottom to fix this.

## Slide 12: Refine layer discretization
1. Select Model | MODFLOW Layer Groups,
2. Change the vertical discretization to 10, 20, and 10 respectively,
3. And set the Method to Increase upward, Uniform spacing and Increase downward.

## Slide 13: This is what you should get

## Slide 14: Education evenings 2018
Practical introduction to groundwater modelling
Computer exercises
04 01 Grid design
Questions? Found an error? Please contact B. Rogiers at brogiers@sckcen.be.